Table of Contents

A disclaimer of liability .......................................................................................................................... 4

Introduction ............................................................................................................................................. 5

Understanding TESLA network .............................................................................................................. 6

T-CAN PRO Diagnostic interfaces ......................................................................................................... 7

Wiring Diagrams - x437 and x437A ....................................................................................................... 8

Tesla Connector x437, x437A Pinouts ................................................................................................... 12

T-CAN Software Installation & Activation ............................................................................................ 13

System requirements ............................................................................................................................... 13

Software download .................................................................................................................................. 13

Installation of the license activation file .................................................................................................. 14

Airbag ECU Crash Data Resetting .......................................................................................................... 22

How it looks Tesla SRS airbag control module and where is located ?................................................... 23

SRS - TESLA MODEL S ........................................................................................................................ 25

SRS - TESLA MODEL X, 3 ................................................................................................................... 29

Adding and learning keys (key-fob) ....................................................................................................... 34

A disclaimer of liability

T-CAN PRO is the first independent device on the market supporting diagnostics in TESLA model S, X and 3 so far.

You must be aware that the use of some T-CAN PRO functions in some countries may be prohibited and against the law.

First of all, what you need to know about the T-CAN PRO before work.

T-CAN PRO:

• The tool is intended only for qualified personnel!

• You must be aware of the risk of loss if something went wrong (learn keys or make adaptations of BMS controller or something else)

• You must have electronic skills which allow you to make adapters yourself and the connection between T-CAN PRO and the vehicle's CAN interface.

• T-CAN PRO uses the CAN network to communicate with the ECU. Therefore, you will not have access to firmware, navigation update, configuration because it cannot be done via CAN. All mentioned things do by LAN on IC,CID not via CAN network.

The author not liable for damage caused or any loss by incorrect use of the T-CAN device.

In addition, he is not liable, if the device's functions are used unlawfully in a country where it is forbidden.

Also the company selling it is not liable for any losses or damage to the goods in question.

Introduction

T-CAN is a young software with small box interface but is constantly being developed.

Can help you solve a few problems with the TESLA car.

As so far, T-CAN PRO can work with ECU TESLA Model S with some function for TESLA Model X and 3

| ALERTS | Alerts on CAN bus ( read and decode alerts codes updated BMS 2018.09.14) |
| --- | --- |
| BDY | Body controller on CAN bus |
| SDM | Supplemental Deployment Module S, X, 3 model (read and decode fault codes, erase stored fault codes and CRASH by Boot mode in S, and diagnostic port in X and 3 |
| SEC | Security controller updated information details 2018.09.14 (Add Keyfob Key) |
| CP | Charging port |
| PARK2 | Parktronic sensors (read and decode fault codes, erase stored fault codes, Updated fault codes 2018.07.08) |
| THC | Thermal controller (Add some features 2018.07.08,Open, close valves for fill or drain cooling fluid , Air purge function) |
| EAS-TAS | Tesla Air suspension System (read and decode fault codes, erase stored fault codes, exit service mode) |
| BMS | Battery control Module (reset alert warnings w163,w026,w152,w153,w023) |
| TPMS | Tyre Pressure Monitor System (read and decode fault codes, erase stored fault codes) |
| ESP | Electronic stability system (read and decode fault codes, erase stored fault codes, Updated fault codes |

Understanding TESLA network

The following diagram of the TESLA “S” network will explain to you what you can use T-CAN PRO for.

T-CAN PRO Diagnostic interfaces

T-CAN has no diagnostic connector x437A so far, but is able to working with this link, just adapter DB15 <-> x437A you must do it yourself.

The white or grey connector x437 is used in TESLA Model S pre September 2015

The blue connector x437A is used in TESLA Model S, X,3 post September 2015

Wiring Diagrams - x437 and x437A

T-CAN Hardware 03 has two separate units: a diagnostic T-CAN PRO unit and a multiplexor. However, T-CAN Hardware 04 has two the same units enclosed in one long housing.

Wiring diagram to use T-CAN v.03 without Multiplexor with x437 connector

applicable for use between T-CAN diagnostic unit and x437 female connector without use a multiplexor.

Wiring diagram to use T-CAN v.03 without Multiplexor with x437A connector

applicable if for some reason you do not want or you cannot use the multiplexor

Wiring diagram to use T-CAN v.03 and v.04 and newer with Multiplexor with x437 connector

applicable directly after purchase because exactly this interface you will get with T-CAN Tool set.

Wiring diagram to use T-CAN v.03 and v.04 and newer with Multiplexor with x437A connector

it applies if you going to use T-CAN tool with Multiplexor with

TESLA Model S post September 2015 and TESLA X,3 with blue connector

Tesla Connector x437, x437A Pinouts

Tesla Diagnostic Port Connector pinout

Pre 2015 Tesla Model S                                            Post 2015 Tesla Model S

Connector x437 white                                                  Connector x437A blue

| 1 = CAN 3 HI - Powertrain Bus | 1 = 12V/5A (F219) |
| --- | --- |
| 2 = CAN 4 HI - Body Faults Bus | 2 = CAN4+ Body Fault |
| 3 = K Bus ISO9141 single wire LIN | 3 = CAN4- Body Fault |
| 4 = CAN 6 HI Chassis Bus | 7 = K/Serial |
| 5 = CAN 2 HI Body Bus | 9 = CAN2 Body + |
| 6 = CAN 3 LO Powertrain Bus | 10 = CAN2 Body- |
| 7 = CAN 4 LO Body Faults Bus | 13 = CAN6+ Chassis |
| 8 = Not used | 14 = CAN6 Chassis- |
| 9 = Reference Ground | 18 = CAN3 Powertrain+ |
| 10 = 12V | 19 = CAN3 Powertrain- |
| 11 = CAN 6 LO Chassis Bus | 20 = GND |
| 12 = CAN 2 LO Body Bus |

T-CAN Software Installation & Activation

System requirements

• Operating system: Microsoft Windows 7/8/8.1/10 (32/64 bit)

• 1 free USB port. 2 or 3.0

Download and install:

1. Main software

T-CAN PRO (date xx.xx.2019) or newer (RAR archive)

2. Drivers USB Serial Port for T-CAN Interface:

Drivers for T-CAN Interface /CDM20824/ (RAR archive)

in some circumstances you may also need to download and install latest drivers CDM20824 USB D2XX drivers for FT232RL , can be downloaded from http://www.ftdichip.com/Drivers/D2XX.htm

The software is working without installation.

So you can just simply create folder and extract software wherever you want and lunch by clicking on executable file “t_can_pro.exe”

Installation of the license activation file

Before you start working with the mentioned software, you have to activate software using license TCAN.bin file that you will receive on your an email address after shopping.

EXAMPLE:

You will received activation file: TCAN000000000xxx.rar

To extract a RAR file, you will need:

WinRAR archiver software: https://www.rarlab.com/download.htm

or free and open source 7-Zip https://www.7-zip.org/

then after extracting files you need to move/copy TCAN.bin file to the directory where is IDMONACT folder

the right path should look as shown in the following:

C:\T-CAN PRO\IDMONACT \TCAN0000000000xx\tcan.bin

visualization for better understanding, step by step

just drag and drop RAR archive file to IDMONACT folder

now you can connect the T-CAN PRO to your PC/laptop

and run executable file