With 2016 the Tesla Model S got an update

Tesla model S has changed the front fascia and now has a similar design as the Model X, adding adaptive LED headlights.

Tesla Model S before face-lifting                              Tesla Model S after facelift               	HID				LED

What's the LED - HID emulator for ?

LED-HID emulator allows you to adapt new LED headlight to older Tesla Model S before facelift.

The emulator converts analogue inputs to digital and transmits to the LED headlights.

With that EMULATOR you can connect LED (New face headlights) to old Tesla Model S with HID lights.

Applies to Tesla model S with old HID lamps only – Tesla Model S 2012 - June 2016

How to connect LED - HID emulator

Before you start the new LED lamps has to be attached

connect all connectors (description below)

1) plug it to the LED lamp

2) plug it to HID-LED emulator

3) connect the emulator power supply to the battery (positive and negative)

- RED +12v positive terminal

- BLACK GND negative terminal

4) Check all connections again.

5) Done !

we strongly recommend using a 15A fuse for protection

Now you can enjoy of new fully working LED headlights

The emulator is working like analog to digital converter (A/D)